## Slide 1: Robust, Precise, and Calibration-Free Shape Acquisition with an Off-the-Shelf Camera and Projector
Chunyu Li, Akihiko Torii, and Masatoshi Okutomi
Tokyo Institute of Technology

## Slide 2: Introduction
Acquiring 3D shapes of real-world objects has attracted significant attention, e.g.
cultural relics:
animal skeletons:
Faro 3d:
Shortcoming: Expensive sensors, requiring professional skills
Image source: english.cntv.cn; Virtual skeletons: using a structured light scanner to create a 3D faunal comparative collection; www.faro.com/ja-jp/

## Slide 3: 3D reconstruction from images
Structure from Motion (SfM)
  Camera poses + sparse 3D point cloud
Multi-View Stereo (MVS)
  Dense 3D point cloud (+ surface model)
Softwares available, e.g. VisualSFM, COLMAP, MVE, …
Pros: Use images (cameras) only
Cons: Requires objects to be well textured

## Slide 4: Structured light system
3DUNDERWORLD-SLS [Gu ‘14]
Project a Structured-light pattern sequence
Pros: Precise, not requiring texture.
Cons:
  Require camera calibration (intrinsic and extrinsic parameters).
  Require to merge 3D point clouds in order to obtain the entire shape

## Slide 5: Proposed method
We combine SfM and structured-light technique.
      Precise, not requiring texture and calibration-free!

## Slide 6: Overview of proposed method
1. Data Acquisition
2. Assigning gray codes to image pixels
3. Matching image pixels
4. 3D reconstruction and loop closure
Camera viewpoint 01
Camera viewpoint 02
・・・
・・・
Camera viewpoint 02
Camera viewpoint 01
Camera viewpoint 01 and 02
Camera viewpoint 01 and 03
・・・
Point cloud

## Slide 7: 1. Data Acquisition

## Slide 8
Step1: Acquiring from multiple views
Schematic of the proposed system

## Slide 9: Step2: Moving the projector
Schematic of the proposed system

## Slide 10: 2. Assigning gray codes to image pixels

## Slide 11: Assigning gray codes to image pixels
0
0
0
1
1
1
0
1
0
0
The decode algorithm is same as [Gu ‘14]
0
0
0
1
1
0
1
0
1
1
Vertical:
0101011001(401)
Horizontal:
0100101100(456)
Decimal number 456401

## Slide 12: 3. Matching image pixels

## Slide 13: At common projector position
  Connect the pixels in all camera viewpoints which have the same code.

## Slide 14: At different projector position
Link the codes located at the same pixel in fixed viewpoint (like the camera viewpoint 02).

## Slide 15: Feature tracks
Camera view 01
Camera view 02
Camera view 03
Camera view 04
Camera view 05
Camera view 06
Camera view 07
Then we can obtain the correspondence of all of the images token around the object.

## Slide 16: 4. 3D reconstruction and loop closure

## Slide 17: 3D reconstruction
SfM using feature tracks computed by gray-code matching
  Estimate the camera poses (camera parameters).
  Compute 3D coordinates by performing triangulation and bundle adjustment.
  Output:
Cameras
3D points

## Slide 18: Loop closure
Loop closure
  Extract the correspondences between the first and last viewpoints. (Using Iterative Closest Point (ICP) algorithm).
  Employ bundle adjustment again with the new correspondences to close the loop.
The first viewpoint
The last viewpoint
The first viewpoint
The last viewpoint
The first viewpoint
The last viewpoint
correspondences

## Slide 19: Experiments

## Slide 20: Experiments
Setup
  iPhone7 (video resolution: 1920 * 1080)
  ASUS P3B data projector (resolution: 1024 * 768)
Setup

## Slide 21: Results: Gundam Model
Google Tango (Tof camera):
Lenovo Phab 2 Pro Smartphone
SfM-MVS:
288 input images
Resolution: 1920 * 1080
VisualSFM, CMVS
Proposed Method
Object

## Slide 22: Results: Plastic bucket
SfM-MVS:
532 input images
Resolution: 1920 * 1080
VisualSFM, CMVS
Google Tango (Tof camera):
Lenovo Phab 2 Pro Smartphone
Proposed Method:
Object

## Slide 23: Conclusions
Proposed a stable and high-accuracy entire shape measurement system based on structured-light and SfM technique.
Require no special devices and just use a standard camera and projector
The performance has been confirmed by several experiments.

## Slide 24
Thanks for your attention.