## Slide 1: Inter-Beat Interval Estimation from Facial Video Based on Reliability of BVP Signals
Yuichiro Maki1, Yusuke Monno1, Kazunori Yoshizaki2, Masayuki Tanaka1,3, and Masatoshi Okutomi1
1Tokyo Institute of Technology 2Olympus Corporation
3National Institute of Advanced Industrial Science and Technology
International Conference of the IEEE Engineering in Medicine and Biology Society (EMBC2019)
July 27, 2019

## Slide 2: Background
Facial video
Blood volume pulse (BVP)
Heart rate (HR)
Inter-beat interval (IBI)
Remote cardiac information measurement from facial video
Non-contact measurement
Low-cost and instant measurement
Multiple subjects measurement
Cardiac information

## Slide 3: What is blood volume pulse (BVP) ?
Video-based BVP acquisition methods extract color change of skin surface.
Camera
Estimation

## Slide 4: HR and IBI
Average HR
Inter-Beat Interval
BVP
0[s]
1.2[s]
2.0[s]
BVP
FFT
t
t
f
HR = 60f’ BPM
f’
1.2 sec
0.8 sec
Derived by
Dominant frequency
Derived by
Peak locations (More challenging)

## Slide 5: HR and IBI
Average HR
Inter-Beat Interval
BVP
0[s]
1.2[s]
2.0[s]
BVP
FFT
t
t
f
HR = 60f’ BPM
f’
1.2 sec
0.8 sec
IBI provides us with HRV parameters.
-> Important clues of many physiological and emotional states such as heart diseases and stress levels.

## Slide 6: Contributions
We have proposed an IBI estimation method from facial video based on reliability of BVP signals.
We have validated our method with a newly constructed 300-fps dataset.
We have launched publicly available IBI estimation dataset and code.

## Slide 7: Poh et al. framework (IEEE TMBE, 2011)
Intensity signals
Time
Time
Time
Input video
FFT
Time
ICA-based BVP estimation
Estimated HR
ICA-based BVP estimation
Input: Multiple temporal intensity signals
Output: Estimated BVP
R
G
B
Estimated BVP

## Slide 8: Poh et al. framework (IEEE TMBE, 2011)
Time
Time
Time
Estimated BVP is NOT stable for IBI estimation.
Input video
Time
Peak detection
Estimated IBI
R
G
B
Intensity signals
ICA-based BVP estimation
Estimated BVP

## Slide 9: Lam et al. framework (ICCV, 2015)
HR
・・・
G channel
Histogram
voting
・・・
・・・
Intensity signals
HR
Random patch sampling
FFT
HR
Estimated HR
FFT
Estimated
HR
ICA-based BVP estimation
ICA-based BVP estimation

## Slide 10: Our IBI estimation framework
・・・
G channel
・・・
・・・
Average intensity
Estimated
IBI
Reliability based BVP selection
Peak detection
We propose reliability-based BVP selection.
Only the most reliable BVP is used for IBI estimation.
ICA-based BVP estimation
ICA-based BVP estimation
Random patch sampling

## Slide 11: Reliability metric
Reliable BVP
Unreliable BVP
Evaluate peak height variance of BVP
Low peak height variance: Reliable
High peak height variance: Unreliable
Low
variance
High
variance

## Slide 12: Peak detection
BVP candidates
Peak detection
IBI calculation
Estimated IBI
t
BVP
Outlier removal
Interpolation
All peaks within the gray band are ignored, assuming that maximum HR is 240 BPM.

## Slide 13: IBI calculation
BVP
IBI
t
t
…
…
Peak detection
IBI calculation
Estimated IBI
Outlier removal
Interpolation
BVP candidates

## Slide 14: Outlier removal
Inlier
BVP
IBI
t
t
…
…
Peak detection
IBI calculation
Estimated IBI
Outlier removal
Interpolation
BVP candidates
Outlier

## Slide 15: Interpolation
BVP
IBI
t
t
…
…
Peak detection
IBI calculation
Estimated IBI
Outlier removal
Interpolation
BVP candidates

## Slide 16: Experiment
Experimental setup
Fluorescent (FL) light
NIR light
Handgrip
Contact PPG
Camera (300fps, VGA)
LED light
Exercise
To vary IBI
10-15 Kg, 60 times/min
Exercise equipment (handgrip)
Example of the frame
Contact PPG

## Slide 17: Experiment
Participants
9 subjects
Relax
Exercise
Relax
60 [s]
60 [s]
60 [s]
Experimental flow
IBI[s]
Time[s]

## Slide 18: Result | Absolute error of IBI
Our proposed patch selection increases accuracy.
Sample: 9 subject 180 sec
Success rate
Improve!

## Slide 19: Result | Sequential IBI
Estimated IBI
Ground-truth IBI
IBI[s]
Time[s]
Estimated IBI and ground-truth IBI are well correlated in both relax and exercise sessions.
Subject 1

## Slide 20: Result | Sequential IBI
IBI[s]
Time[s]
IBI[s]
Time[s]
Subject 1
Subject 2
Estimated IBI
Ground-truth IBI
Estimated IBI
Ground-truth IBI

## Slide 21: Conclusion
We have proposed an IBI estimation method from facial video based on reliability of BVP signals.
We have validated our method with a newly constructed 300-fps dataset.
We have launched publicly available IBI estimation dataset and code.

## Slide 22: Dataset and code
Dataset
  Videos of 9 subjects
  Contact PPG data
  * You have to agree End User License Agreement to download the dataset.
  [Project page: http://www.ok.sc.e.titech.ac.jp/res/VitalSensing/remoteIBI/index.html ]
Code
  Patch sampling-based candidate BVP acquisition
  Reliability-based BVP selection
  IBI calculation
  Some other useful functions
  [GitHub: www.github.com/ymonno/RemotePPG ]
Project page
Example of the dataset frame